## Slide 1
Lighting Module — PCB Arrangement
Two interlocking head-lamp PCBs frame a central logo PCB inside the lamp housing
LOGO PCB
HEAD LAMP PCB
HEAD LAMP PCB
Lamp housing
Head Lamp PCB ×2
Two C-shaped boards interleave around the centre. Each wraps three sides, so together they trace a continuous light contour.
Logo PCB
Central board dedicated to the illuminated logo, set off from both head-lamp boards by a uniform clearance gap.
Lamp housing
The outer frame nests all three boards with even clearance for assembly tolerance and thermal expansion.
One outline, used twice. The two head-lamp PCBs share the same shape rotated 180°: one part number, one panel design, one stencil.

## Slide 2
DRL Module — LED Layout & Interconnect
Eight LEDs on each DRL PCB, with light-emission arrows rotated to each board's orientation
LED1
LED2
LED3
LED4
LED5
LED6
LED7
LED8
LED1
LED2
LED3
LED4
LED5
LED6
LED7
LED8
LED1
LED2
LED3
LED4
LED5
LED6
LED7
LED8
DRL PCB 1 light ↑
DRL PCB 3 light ↓
DRL PCB 2
light →
Wire harness (8-way)
L4
Driver
Layout at a glance
Three DRL PCBs form a C-shaped outline around the lamp opening.
8 LEDs per board; the string runs PCB 1 → PCB 2 → PCB 3.
Flex jumpers bridge both corners — no board-to-board connectors.
Each board's light arrows follow its own orientation: ↑, →, ↓.
Legend
LED + light
Flex jumper
PCB trace
Harness wire

## Slide 3
Why This PCB Architecture Works
Design rationale, reliability, and how the layout supports EMI/EMC compliance
Design justification
1
Modular rigid boards
Three straight PCBs follow the lamp contour, so panels nest efficiently. The head-lamp pair reuses one outline, which cuts tooling and part count.
2
Flex jumpers, not connectors
Polyimide flex removes crimps and board-to-board headers. Fewer contacts improve vibration and thermal-cycle reliability (ISO 16750-3) and let the module fold into the housing.
3
Series LED string
Every LED carries the same current, so luminance and colour stay uniform across all three boards. The driver regulates one current, and no ballast resistors are needed.
4
Distributed thermal load
24 LEDs spread over three boards keep power density low. Copper pours and thermal vias lower Tj, which protects lumen maintenance and LED life.
Why EMI / EMC compliance is met
Noise source kept off the lamp boards. The switching L4 driver sits on its own board, so the long DRL PCBs carry only DC LED current and have no high dv/dt nodes to radiate.
Small current loops. Supply and return run as adjacent pairs in the harness and flex, which minimises loop area and cuts both radiated emissions and pickup.
Solid reference plane. Each rigid PCB has an unbroken ground pour with stitching vias along its edges, so no return current crosses a slot.
Filtered and dithered driver. Input π-filter with CM choke, spread-spectrum switching and slew-rate controlled PWM dimming lower peaks in the CISPR 25 AM/FM bands.
Protected entry points. TVS and 100 nF/1 nF decoupling at each connector absorb ESD and load-dump transients before they reach the LEDs.
Target standards
UN ECE R10
Vehicle EMC approval
CISPR 25 Cl. 5
RF emissions (CE / RE)
ISO 11452-2/-4
RF immunity (ALSE, BCI)
ISO 7637-2
Supply-line transients
ISO 10605
ESD ±8 kV / ±15 kV